Minimicro II Design Documents and Consideration
The Minimicro architecture contains a number of instructions that require very little effort to implement in Verilog, however there remain several instructions that require more involved effort.

Processor outputs/inputs (excluding the obvious, like clk, etc):
MEMOUT – Memory output, 16 bits. This is connected to a multiplexer for the following values
1. The current value of the C register (or whatever value that represents within the pipeline.
2. The current value of the program counter plus one (this is for call instructions)
MEMWRITE – Whether to write the specified memory output.
MEMIN – Memory input, 16 bits.
ADDR – Current address to fetch. This is multiplexed to three different objects within the processor,
1. The instruction counter
2. The stack pointer
3. The combined A and B
All of the values presented, except for the ADDR pins, are to be connected directly to registers, which are then, in turn, behaviorally modeled.